## Slide 1: Tobit Analysis of Vehicle Accident Rates on Interstate Highways
Panagiotis Ch. Anastasopoulos, Andrew Tarko, and Fred Mannering

## Slide 2: Accident Frequency Modeling
Number of accidents on a roadway segment per some unit time.
As a function of roadway geometrics, traffic and weather conditions
Has been modeled with:
  Poisson regression
  Negative Binomial
  Zero-inflated Poisson and Negative Binomial
  Random Parameters Negative Binomial
2
Notes: Mnl,nl,ml
Talk about heteroskadastic issues
Ordered versus non-ordered

## Slide 3: Consider a different approach:
Instead of looking at “frequency” of accidents, consider accident rates (accidents per 100 million VMT)
Advantages:
  Accidents per 100 million VMT is a commonly reported statistic in government reports and the popular press
  Provides an intuitive appeals for interpretation of results
3
Notes: 3
Mnl,nl,ml
Talk about heteroskadastic issues
Ordered versus non-ordered

## Slide 4: Problems with an accident rate approach:
Variable is now continuous and “censored” (many roadway segments will have zero observed accidents in a specified time period)
OLS regression is thus not appropriate
Option: Tobit model
4
Notes: 4
Mnl,nl,ml
Talk about heteroskadastic issues
Ordered versus non-ordered

## Slide 5: Censored data
Censored data: Data can be at a lower threshold (left censored), an upper threshold (right censored), or both.
Censored data differ from truncated data –truncated data only have non-limited values available (censored data provide information on limited data as well).
5
Notes: 5
Mnl,nl,ml
Talk about heteroskadastic issues
Ordered versus non-ordered

## Slide 6: Tobit model (James Tobin, 1958) (1981 Nobel Laureate)
The tobit model is expressed (for roadway segment i) using a limit of zero (which will be the case for our analysis) as:
6
Notes: 6
Mnl,nl,ml
Talk about heteroskadastic issues
Ordered versus non-ordered

## Slide 7: Where:
where N is the number of observations,
Yi is the dependent variable (accidents per 100-million vehicle miles traveled),
Xi is a vector of independent variables (traffic and roadway segment characteristics),
β is a vector of estimable parameters, and
εi is a normally and independently distributed error term with zero mean and constant variance σ2.
It is assumed that there is an implicit, stochastic index (latent variable) equal to which is observed only when positive.
7
Notes: Parochial Investigations in General
  Human Factors
  Police Enforcement Activities
  Specific Injury Types
  Vehicle Types
Specification Bias
Double Pair Comparison
Multi-Variate Time Series
Log-Linear
Discriminant Analysis
Logistic Regression
Multinomial Logit
GEV Structures
Nested Logit
Systems Methods - FIML Evidenced in Demand Research
Safety Research
  Did Not Investigate Policy Variables in Severity Context
Methodologies & Issues in Nested Logit in Transportation
These uses have applied a mixed logit without repeated choice (Ben-Akiva, Bolduc and Bradley 1993, Ben-Akiva and Bolduc 1996; Brownstone and Train 1996; and Bhat 1998). A number of authors have determined choice probabilities by integration of the logit function over the unobserved terms (see Boduc, Fortin and Fournier 1993; Berkovec and Stern 1991; and Train, McFadden, and Goett 1987). In these studies they allowed the unobserved terms to differ from the random parameters of the observed attributes.
Relatively recent research conducted by Revelt and Train (1997), Train (1999), Brownstone and Train (1999), McFadden and Train (2000), Bhat (2001), has demonstrated the effectiveness of a methodological approach that can explicitly account for the variations (from one roadway segment to the next) in the effects that variables have on injury-severity proportions – the mixed logit model (also referred to as the random parameters logit model).

## Slide 8: Tobit Model is estimated by maximum likelihood estimation
With likelihood function:
8
Notes: 5
[1] For a statistical model of the likelihood of an accident occurring, the reader is referred to our earlier work on accident frequencies (Milton and Mannering 1996; Shankar, Milton and Mannering 1997; Shankar, Albin, Milton and Nebergall 2003).
[2] This differs from the Shankar, Mannering and Barfield model in which four discrete severity categories were evaluated because insufficient fatality data was available to draw reasonable conclusions.
[3] For the remainder of the document severity refers to the most severe consequence.

## Slide 9: Empirical setting
337 segments (Indiana Interstates)
  Individual characteristics of each section aggregated into segment-level observations
Five-year accident data (January 1995 to December 1999)
Segment-defining information included
  shoulder characteristics (inside and outside shoulder presence and width and rumble strips),
  pavement characteristics (pavement type),
  median characteristics (median width, type, condition, barrier presence and location),
  number of lanes,
  and speed limit.

## Slide 10: Dependent variable:
  Accident Ratei is the number of accidents per 100-million VMT on roadway segment i,
  Year denotes the year (from 1 to 5 representing 1995 to 1999),
  AccidentsYear,i is the number of accidents,
  AADTYear,i the average annual daily traffic,
  Li the length of roadway segment i.
10

## Slide 11: Findings
11

## Slide 12: Pavement Characteristics:
  (-) High-friction indicator variable (1 if all 5-year friction readings are 40 or higher, 0 otherwise),
  (-) Smooth pavement indicator variable (1 if 5-year IRI readings are below 75, 0 otherwise),
  (-) Excellent rutting indicator variable, (1 if all 5-year rutting readings are below 0.12 inches, 0 otherwise) ,
  (-) Good rutting indicator variable (1 if all 5-year average rutting readings are below 0.2 inches, 0 otherwise) ,
  (+) Average PCR indicator (1 if greater than 95, 0 otherwise)
12
Notes: 12

## Slide 13: Geometric Characteristics:
  (-) Median width indicator variable (1 if greater than 74 feet, 0 otherwise),
  (-) Median barrier presence indicator variable (1 if present, 0 otherwise),
  (-) Inside shoulder width indicator variable (1 if 5 feet or greater, 0 otherwise) ,
  (-) Outside shoulder width (in feet),
  (-) Number of bridges (per road section)
13
Notes: 13

## Slide 14: Geometric Characteristics (cont.):
  (-) Rumble strips indicator variable (1 if both inside and outside rumble strips are present, 0 otherwise)
  (-) Number of vertical curves per mile,
  (+) Ratio of the vertical curve length over the road section length (in tenths),
  (-) Horizontal curve's degree curvature indicator variable (1 if average degrees per road section is greater than 2.1, 0 otherwise) ,
  (+) Number of ramps in the driving direction per lane-mile.
14
Notes: 14

## Slide 15: Traffic Characteristics:
  (-) AADT of passenger cars (in 1,000 vehicles per day),
  (-) Average daily percent of combination trucks.
15
Notes: 15

## Slide 16: Summary
Tobit regression is a plausible method for accident-rate analysis analysis
Approach provides an intuitive interpretation of accident rate data
Tobit models avoid the theoretical problems that some have with zero-inflated models
16
Notes: 1990-1994 1991-1994 1990 Calculated Chi-Square Critical chi-square value at 95% confidence interval
No of Obs. 1375 825 550 chicalc chi criticial
LL -21978.74 -13229.76 -8747.01 3.94 12.9